## Slide 1: EM2E Chassis service modes SM 3122 785 10310
Service Modes
Service Alignment Mode (SAM)
Can be activated by RC by dialling ‘062596’ + ‘OSD’,
by ComPair / DST or short-circuiting item 4005 on SSB.
* Following slides will show the Service Alignment Mode (SAM) menu structure of the EM2E chassis.
* The first slide will show the DST opening menu.

## Slide 2
The Service Entry Menu by DST.
Service Entry
 Enter password and press OK: - - - -
* - - -
* * - -
* * * -
* * * *
Dial the password by DST or a RC
3
1
4
0
Press OK!

## Slide 3
Date: May 11 2000 Id: EM2E_11.4_02391
Operation Hours: 00000.0
Errors: No Errors
Defect. Module: Unknown
 Service
Reset Error Buffer
Functional Test
Alignments
Dealer Options
 Service
PC simulated menus from 32PW8506 wide-screen TV set.
This is the start menu window we will see in SAM.

## Slide 4
This type of information will be shown if there is any error codes detected.
Date: May 11 2000 Id: EM2E_11.4_02391
Operation Hours: 00000.0
Errors: 5 0 0 0 0
0 0 0 0 0
Defect. Module: +8 V Supply
 Service
Reset Error Buffer
Functional Test
Alignments
Dealer Options
 Service
Select and press ’Reset Error Buffer’.

## Slide 5
Service Default Mode (SDM)
Service Modes
Can be activated by RC by dialling ‘062596’ + ‘MENU’,
by ComPair / DST or short-circuiting item 4006 on SSB.
N.B. In this mode all TV settings are fixed (default) as follows!
* Tuned frequency 475.25 MHz
* TV-systems for BGLM sets are set to BG
* Picture settings (contrast, brightness, colour & hue are
set to 50% value.
* All sound settings to 50% value except volume to 25%
* All service unfriendly modes are disabled (like sleep timer,
child lock, blue mute, AVL and SDLP).

## Slide 6
Service Modes
Customer Service Mode (CSM)
This menu is meant to show the actual TV settings and other functional information for a customer if requested by service when ‘a fault or a malfunction’ has occurred.
This CSM menu is read only menu, so NO modification to any settings can be done by this menu.
To activate it, press simultaneously the ‘MUTE’ key on RC
and the ‘MENU’ key on the TV set minimum of 4 seconds.

## Slide 7
Service Modes
Customer Service Mode (CSM)
CUSTOMER SERVICE MENU 1
1 SW Version EM2E_11.5_02431
2 Code 1 (error code) No Errors
3 Code 2 (error code)
4 LS Volume 7
5 LS Brightness 28
6 LS Contrast 48
7 LS Colour 31
8 LS Headphone 12
9 Sharpness 3
10 Dolby 0
11 Surround mode
11a Tuner Frequency 203 MHz


## Slide 8
Service Modes
Customer Service Mode (CSM)
CUSTOMER SERVICE MENU 2
13 Centre Volume 11
14 DNR Off
15 Noise Figure 15
16 Digital Option Digital Scan
17 Colour System PAL
18 TV System BG
19 Audio System NICAM
20 Tuned Bit Off
21 Speaker Config. 0
22 Digital Sources None

Range 0 - 255, 0 = no noise, 255 = noise
Important for DVD

## Slide 9
Error Code Table

## Slide 10
Service Modes
Reading error codes from the buffer. With DST
If for example the following error codes are found:
Error position; 1 2 3 4 5
Error Codes: 12 9 5 0 0
Error Codes
This is what we can read from the buffer.
The latest error is in position 1, next in pos. 2 etc.
The error codes are shown in SAM, 10 codes in two rows, and the selected one is displayed in SDM by blinking standby LED
Try these

## Slide 11
Service Modes
Reading error codes from the buffer
Error position; 1 2 3 4 5
Error Codes: 12 9 5 0 0
Error Codes
A long blink means (ten) and short blinks (units).
The error code is repeated until the set is shut off.
---------------
The standby
LED
10
11
12
10
11
12
If the first error position is chosen……then..
The standby LED will blink the value of the error code..
If the first error position is chosen……then..
The standby LED will blink the value of the error code..
In this case we read the error code 12 which means
Tuner protection..

## Slide 12
Service Modes
Reading error codes from the buffer
Error position; 1 2 3 4 5
Error Codes: 12 9 5 0 0
Error Codes
A long blink means (ten) and short blinks (units).
The error code is repeated until the set is shut off.
Or if you choose the second error position…...
The standby LED will blink the value of the error code..
--------------------
The standby
LED
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Or if you choose the second error position…...
The standby LED will blink the value of the error code..
So in this case we read the error code 9, which means
X-ray protection

## Slide 13
Service Modes
Reading error codes from the buffer
Error position; 1 2 3 4 5
Error Codes: 12 9 5 0 0
Error Codes
A long blink means (ten) and short blinks (units).
The error code is repeated until the set is shut off.
Or if you choose the third error position…...
The standby LED will blink the value of the error code..
------------------------
The standby
LED
1
2
3
4
5
1
2
3
4
5
Or if you choose the third error position…...
The standby LED will blink the value of the error code..
In this case the error code is 5 which means,
+8 V Supply.

## Slide 14
Service Modes
Reading error codes from the buffer
Error position; 1 2 3 4 5
Error Codes: 12 9 5 0 0
Error Codes
A long blink means (ten) and short blinks (units).
(In this case the DST display will stay blanked).
If you choose any other error position which contains zero (0). The standby LED will NOT blink..
------------------------------
The standby
LED
or..

## Slide 15
Service Modes
Error Codes with DST
Always start faultfinding with DST like this;
1. Press the ’Diagnose’ button on the DST!
2. Press the digit keys ’99’!
3. Press the ’OK’ key!
Now the DST transmits a code to erase all error codes in the set. Switch off the set with the mains switch and start it again with the mains switch. Wait until the standby LED starts blinking!

## Slide 16
Service Modes
Reading error codes with DST from the buffer
Error position; 1 2 3 4 5
Error Codes:
Error Codes
If you use DST for fault finding read all error codes
from the left to the right until the first zero is found!
---------------
---------------
12 9 5 0 0
12 9 5 0 0
Start reading the error codes from the position number one !
Start reading the error codes from position number one !
Write down the error code from the position one

## Slide 17
Service Modes
Reading error codes with DST from the buffer
Error position; 1 2 3 4 5
Error Codes:
Error Codes
If you use DST for fault finding read all error codes
from the left to the right until the first zero is found!
12 9 5 0 0
Read the error code from the position two !
Read the error code from the position two !
Write down the error code number two !
--------------------
--------------------
12 9 5 0 0

## Slide 18
Service Modes
Reading error codes with DST from the buffer
Error position; 1 2 3 4 5
Error Codes:
Error Codes
If you use DST for fault finding read all error codes
from the left to the right until the first zero is found!
12 9 5 0 0
Read the error code from the position three !
Read the error code from the position three !
Write down the error code number three !
-------------------------
-------------------------
12 9 5 0 0

## Slide 19
Service Modes
Reading error codes with DST from the buffer
Error position; 1 2 3 4 5
Error Codes:
Error Codes
If you use DST for fault finding read all error codes
from the left to the right until the first zero is found!
12 9 5 0 0
Read the error code from the position four !
Read the error code from the position four !
-------------------------------
-------------------------------
12 9 5 0 0
Now, we have found the first zero
5
5
5
and can start looking for the fault from the rightmost error code position,
which is in this case position 3,
error 5 = +8V Supply !