## Slide 1
SECTION 1. TEST METHOD
1.1 HANDSET
1. Instrument for Test
1) MULTIMETER
2) AC VOLT METER (ACVM)
3) AUDIO FREQUENCY GENERATOR (600ohm OUTPUT)
4) STORAGE OSCILLOSCOPE
5) TELEPHONE ANALYZER
or 20Hz RING GENERATOR with ADJUSTABLE OUTPUT LEVEL
6) R/S DIGITAL RADIOCOMMUNICATION TESTER (CMD60)
or HP8932A(B) DECT Test Set
5

## Slide 2
2. Standard Test Condition
1) STANDARD VOLTAGE
(1) BASESET UNIT ........................ INPUT : AC 230V ±10%, 50Hz
OUTPUT: DC 9V 500mA
AC 9V 300mA
(2) HANDSET UNIT ............................... DC 3.6 ± 0.1V
2) TEMPERATURE .................................... 25 ± 5℃
3) CHANNEL FREQUENCY
CHANNEL FREQUENCY
0 ------------------------------------- 1897.344 MHz
1 ------------------------------------- 1895.616 "
2 ------------------------------------- 1893.888 "
3 ------------------------------------- 1892.160 "
4 ------------------------------------- 1890.432 "
5 ------------------------------------- 1888.704 "
6 ------------------------------------- 1886.976 "
7 ------------------------------------- 1885.248 "
8 ------------------------------------- 1883.520 "
9 ------------------------------------- 1881.792 "
4) MODULATION ..................................... GFSK Bbt = 0.5
5) CHANNEL MULTIPLEX .............................. TDMA
6) DUPLEX METHOD .................................. TDD
7) TELEPHONE LINE IMPEDANCE ....................... 600Ω
8) CHANNEL GRID ................................... 1.728MHz
9) BIT RATE ....................................... 1152Kbps
10) VOICE CODING .................................. ADPCM
11) TRANSMITTED POWER ............................. 250mW(Peak)
6

## Slide 3
3. Register of Handset
1) Press the <Paging Key> in Base more than 15 secs until beep sound is heard.
-. After a reset of the Base, the Base is set automatically to register mode.
2) Press the [F/R] key on the Idle Mode and select the “H-REGISTER” Display
3) Press the [O.K] key on the “H-REGISTER” Display and select the “H-REGISTER”
Menu.
4) “SEARCH BS 1” is displayed. Press the [F/R] key, the Baseset Number changes
from 1 to 4. Searching Baseset Number is displayed, select after pressing the
[O.K] key.
5) After the Handset automatically searches, if the RFPI Code is displayed, the
“PIN : “ is displayed. This RFPI Code is different per a Handset.
6) If the “PIN: ” is displayed, input the PIN Code. After inputting PIN Code
4(four) digits(default : 1590), press the [O.K] key.
7) Returned to the “H-REGISTER” Menu.
7
Figure 1 Register Function Flow

## Slide 4
4. Entering TEST MODE
1) Handset test mode
(1) Press the power key and make power off.
(2) The [ESC] key must be pressed and then power key pressed at the same
time.
(3) 1  T6 2  T10 is displayed.
-. It means that T6 is TBR6 mode and T10 is TBR10 mode.
(4) Press the number 1 to enter TBR6 test mode.
(5) If test mode made a success, valid tone sounds and antenna symbol
displayed.
(6) When you want to escape the test mode, press the power key.
2) Base test mode
(1) Pull out the power connection cable.
(2) Press the paging key, and then connect the power adaptor cable.
(3) At this time, you must press the paging key continuously during about 5~6
seconds.
(4) And then you can hear the bell sound.
(5) If you hear the bell sound, you detach the paging key.
(6) And then test mode Entered automatically.
(7) When you want to escape the test mode, pull out the power connection
cable.
8

## Slide 5
5. Test for Handset
1) Preparation
(1) Adjust the voltage of power supply to DC 3.6V.
(2) The [ESC] key must be pressed and turn the power on simultaneously.
(3) 1T6 2T10 is displayed, and press the number 1 to enter TBR6 test mode.
* Disassemble the antenna.
(4) Connect 50Ω coaxial cable to antenna part of RF board.
(5) Connect the coaxial cable to DIGITAL RADIOCOMMUNICATION TESTER (CMD60).
2) Check the below items of the each channel and slot.
(1) TX Frequency Accuracy : ±50KHz.
(2) Frequency Deviation Limit : ±202 ~ ±403KHz
(3) Frequency Drift : ±10KHz
(4) Jitter : <1usec
(5) NTP (Normal Transmitter Power) : 23±2dBm
(6) Bit Error Test : 0.001% (TX Level : -83dBm)
(7) Power Time Mask (Rise/ Middle/ Fall) : Pass
3) Test for Low Battery
(1) Turn the power supply switch off/on.
(2) Decrease the voltage to check that the point which Beep tone is heard
below DC 3.4±0.1V .
9

## Slide 6
6. Test for Baseset
1) Preparation
(1) Adjust the voltage of power supply to 9VDC 500mA.
(2) Press the paging key, and then supply the power.
(3) At this time, you must press the paging key continuously during about 5~6
seconds. and then you can hear the bell sound. If you hear the bell sound,
you detach the paging key.
* Disassemble the antenna.
(4) Connect 50Ω coaxial cable to antenna part of RF board.
(5) Connect the coaxial cable to DIGITAL RADIOCOMMUNICATION TESTER (CMD60).
2) Check the below items of the each channel and slot.
(1) TX Frequency Accuracy : ±50KHz.
(2) Frequency Deviation Limit : ±202 ~ ±403KHz
(3) Frequency Drift : ±10KHz
(4) Jitter : <1usec
(5) NTP (Normal Transmitter Power) : 23±2dBm
(6) Bit Error Test : 0.001% (TX Level : -83dBm)
(7) Power Time Mask (Rise/ Middle/ Fall) : Pass
3) Test for Ring
(1) Set the normal mode by entering power to base and handset.
(2) Adjust ring output Telephone Analyzer to 20Hz, 38Vrms and connect base
to tel. line.
(3) Check the ring is occurred in Ringer of handset when the output of ring
is started in Telephone Analyzer.
10